## Slide 1
DESIGN COORDINATION
Łukasz Wesołowski : Pawel Mika
16-05-2022

## Slide 2
SCHEMATIC DESIGN OPTIMIZATION – material / panel sizes:
Design coordination
Łukasz Wesołowski, Paweł Mika
Options for mass timber fabricators and suppliers
Maximize panel sizes to minimize machine cutting, material waste and costs.
Determine the thickness and grades of roof/floor panels based on preliminary loading. Minimize the thickness of floor/roof panels to control costs.
Approach mass timber design as a modular system.
For panels sourced from overseas, shipping container size limits will govern maximum panel sizes.

## Slide 3
OPTIMIZATION – system coordination:
Design coordination
Łukasz Wesołowski, Paweł Mika
Structure, vibration, fire resistance, acoustics issues for the thickness of the floor/roof panels. These areas usually have the biggest influence on cost.
Coordinate the structure, vibration, fire resistance and acoustic systems. Meet with the project’s consultants/experts to discuss system options and how each impacts the others.
Correlate acoustic and fire-resistance solutions. (They are interdependent.)

## Slide 4
OPTIMIZATION – structural systems:
Design coordination
Łukasz Wesołowski, Paweł Mika
Review the sequencing of installation. Do the lateral systems need to be installed prior to the mass timber?
Which are the best structural modules for designed function? Less columns, more columns but lower beams

## Slide 5
OPTIMIZATION – fire resistance:
Design coordination
Łukasz Wesołowski, Paweł Mika
Optimize the construction type to minimize fire rating impacts. Taller mass timber buildings generally require higher fire-resistance ratings, which may impact timber sizes and material optimization.
Consider fire protection approaches and what should be discussed with the Authority Having Jurisdiction (AHJ) during design. AHJs may be unfamiliar with mass timber systems. Early pre-application meetings can help to align expectations and mitigate concerns far in advance of permit application.

## Slide 6
OPTIMIZATION – acoustics:
Design coordination
Łukasz Wesołowski, Paweł Mika
Consider floor topping options and finishes.
Determine how the wet vs. dry weight of toppings impacts schedule and mass of structure.
Decide whether the mass timber floor/roof panels will be exposed on the ceiling side or concealed.
Consider the minimum level of acoustical performance required by code and expected by the owner/occupant

## Slide 7
OPTIMIZATION – finish quality:
Design coordination
Łukasz Wesołowski, Paweł Mika
Start to consider the appearance of exposed mass timber elements and the species available from different fabricators. Selecting species provided by local fabricators will typically yield shipping/transportation cost savings.
Specify desired finish grades (architectural, industrial, etc.) for budgeting purposes.
Work with potential manufacturers to determine their appearance grade options and associated cost premiums in order to arrive at a solution that meets both aesthetic goals and budgetary constraints

## Slide 8
DESIGN DEVELOPEMENT OPTIMIZATION – material / panel sizes:
Design coordination
Łukasz Wesołowski, Paweł Mika
Check with manufacturers for available panel sizes/spans. Machinery press sizes or the optimization of raw material sizes can influence panel sizes. Most manufacturers can produce panels in symilar lengths
For large panel/member sizes, consider transportation and shipping.
For competitively bid projects, size grids for a variety of manufacturer options.
Are there slight adjustments to the grids that can be made to help control costs?

## Slide 9
OPTIMIZATION – system coordiantion:
Design coordination
Łukasz Wesołowski, Paweł Mika
Consider prefabricated exterior and interior wall elements that preserve the schedulesavings achieved by the structure

## Slide 10
OPTIMIZATION – fire resistance:
Design coordination
Łukasz Wesołowski, Paweł Mika
For exposed panels, fire resistance provided by charring of wood can be calculated. Some manufacturers also have tested assemblies

## Slide 11
OPTIMIZATION – MEPF Systems:
Design coordination
Łukasz Wesołowski, Paweł Mika
Compare a completely prefabricated approach for incorporating MEPF and fire protection systems to field accommodation techniques and decide on the best approach for your project.
With early engagement/design-assist, it is possible to prefabricate many openings and interface points that are much less costly and less prone to risk (damage, error, debris, etc.) than when completed in the field. Seek MEPF contractors skilled in prefabrication of their respective areas (piping, units, duct, etc.).
Consider solutions to accommodate openings without cutting holes in panels (i.e., at ends of panels or routing above/below). Also consider MEPF layout in structural grid placement.

## Slide 12
OPTIMIZATION – finish quality:
Design coordination
Łukasz Wesołowski, Paweł Mika
Obtain material samples and consider finish grade and coatings. Specify several “range and finish” samples, perhaps 6 feet by 6 feet to convey an accurate sense of the outcome.
For cost savings, are there areas where industrial grade appearance can be specified?
Consider surface coatings that can be added for protection during construction, durability, staining, etc. Discuss coatings with fabricators and the GC. Consider whether the options are applied in the shop or field

## Slide 13
OPTIMIZATION – specification:
Design coordination
Łukasz Wesołowski, Paweł Mika
Determine the thickness of panels, number of laminations, grade/species, finish, etc.
Use the manufacturer’s standard product options to help control costs.
Consider protection of steel connectors during construction (paint/primer). Prevent rust stains on exposed wood by priming connectors.
Protect panels during construction with sheathing and by taping seams; cover all end grains/joints; specify shop-applied sealants.
Specify a moisture mitigation plan during construction stating that the timber is to be protected.

## Slide 14
OPTIMIZATION – specification:
Design coordination
Łukasz Wesołowski, Paweł Mika
Costs of stainless/galvanized connections vs. a shopprimed finish can be significant. Consider the cost of these special materials/coatings vs. protection in storage and once in place to mitigate staining.
Consult with fabricators for standard specifications

## Slide 15
OPTIMIZATION – key details:
Design coordination
Łukasz Wesołowski, Paweł Mika
Consider panel-to-panel joint connection options. Determine which is the most appropriate for the project overall, including installation speed, lateral forces, and overall panel length to minimize waste.
For beam-to-column joints:
• Consider whether connections will be concealed or exposed. Where members such as beams, columns and floor/roof panels require a fire-resistance rating, connections between members must have sufficient protection to provide the same fire-resistance rating.
• Evaluate shrinkage and consider continuous columns or steel post stubs.
• Consider prefabricated vs. custom fabricated hangers and the need to CNC timber to accommodate hangers and hardware.

## Slide 16
OPTIMIZATION – key details:
Design coordination
Łukasz Wesołowski, Paweł Mika
For column-to-foundation details:
• Consider prefabricated/preinstalled anchors for quick installation.
• Allow for field adjustment to accommodate tolerances of different materials.
• Detail for moisture and insect protection.
Detail for durability and keep moisture from building up, especially at end grains and joints.
Tolerances of mass timber are much tighter than other materials. Consider tolerances and discuss details with the builder and fabricators of all trades.
Determine how tolerances will be accommodated at the foundation/base level of the project. This area has the greatest potential for differences.

## Slide 17
OPTIMIZATION – key details:
Design coordination
Łukasz Wesołowski, Paweł Mika
Hold a preconstruction coordination meeting with the GC, foundation subcontractor, and mass timber manufacturer/designer to address tolerances and base connections. This is a mandatory best practice with steel (AISC) and structural precast concrete (PCI) and should be the same for mass timber

## Slide 18
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 19
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 20
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 21
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 22
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 23
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 24
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 25
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 26
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 27
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 28
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 29
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 30
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 31
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 32
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 33
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 34
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 35
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 36
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 37
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 38
Design coordination
Łukasz Wesołowski, Paweł Mika

## Slide 39
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Long Beam Short Deck

## Slide 40
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Short Beam Long Deck

## Slide 41
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Beams and Girders

## Slide 42
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Two-Way Beams

## Slide 43
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Reciprocal Frame

## Slide 44
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Point Supported CLT

## Slide 45
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Wide Flat Beams – Beams on the Bottom

## Slide 46
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT proncipals:
Wide Flat Beams – Beams on Top

## Slide 47
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Wide Flat Beams – Beams Flush

## Slide 48
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT proncipals:
Staggered Deck

## Slide 49
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Cassette

## Slide 50
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Triple Beam

## Slide 51
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Stressed Skin Lattice

## Slide 52
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Timberconcrete

## Slide 53
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Timberconcrete

## Slide 54
Design coordination
Łukasz Wesołowski, Paweł Mika
CLT, NLT, DLT principals:
Timberconcrete

## Slide 55
Design coordination
Łukasz Wesołowski, Paweł Mika
Fire safety (widths, divisions)

## Slide 56
Design coordination
Łukasz Wesołowski, Paweł Mika
Fire safety
(widths, divisions)