## Slide 1
02 Structural Systems
Elements (Building Mechanics)
di matthias doubek, bsc
civil engineer, master carpenter
  SUSTAINABLE, HIGH-PERFORMANCE BUILDING SOLUTIONS IN WOOD
  2020-1-LV01-KA203-077513
ERASMUS+ Strategic Partnerships For Higher Education
Timber Construction

## Slide 2: about
education
  Higher Technical College for Timber Technologies – HTBLuVA Mödling
  BSc Civil Engineering and Construction Management - FH Campus Wien
  MSc Construction and completion of Large-scale International Projects- FH Campus Wien
  Postgraduate Student - Sustainable Engineering - University of Exeter (UK)
  Official qualification master carpenter
  Official qualification master builder
  Official qualification property developer
  Official qualification Civil Engineer
Awards
  FH Best Paper Award
  Nomination for Timber Construction Price Lower Austria
  National Steel Construction Austria
Berufspraxis
  5 years site engineer timber construction
  15 years Planning activity for architects and construction engineers (mainly planning, structural engineering, building physics and site management)
  11 years freelance lector
  9 years self employed as consultant, since 2016 konstrukt:ING – konstruktive Ingenieure GmbH
about

## Slide 3: what we do

## Slide 4: timber technology

## Slide 5: structure of wood

## Slide 6: microscopic structure of softwood

## Slide 7: miroscopic structure hardwood

## Slide 8: species of wood for timber constructions
used for
shipbuilding
furniture
terrace
weathered and heavily exposed components
special properties
Very resistant to insect and fungal attack
Beech
Oak
used for
veneers
furniture
woodturner objects
e.g. „Baubuche“ (laminated veneer lumber, laminated into beams, boards and panels) - https://www.pollmeier.com/products/baubuche-about#gref
special properties
Easily to steam-bend
used for
Common buliding wood
(also glued laminated timber)
Pulpwood (paper uses)
special properties
Fast growing
Spruce

## Slide 9: Species of wood for timber constructions
used for
Common buliding wood
(also glued laminated timber)
furniture
special properties
Fast growing
silver fir
used for
Lumber and construction
(also glued laminated timber)
furniture
special properties
Blue fungus
used for
Common buliding wood, esp. Outdoor
furniture
terrace
(small) windows
Furniture
special properties
Durable qualities
pine
larch

## Slide 10: physics – wood moisture equilibrium
Bound water
free water
Water saturation
fiber saturation
Total dryness

## Slide 11: Hygroskopic balance

## Slide 12: dimensionsstabilisierende maßnahmen

## Slide 13: Natural durability
https://www.structuraltimber.co.uk/assets/InformationCentre/eb1.pdf

## Slide 14: Natural durability

## Slide 15: Constructive wood protection

## Slide 16: baustoffe und produkte

## Slide 17: Constructive solid wood

## Slide 18: Layer material cross laminated timber / laminated veneer timber

## Slide 19: Chip material / i-beam

## Slide 20: Planed goods

## Slide 21: Solid wood wide glued / three-layer board plywood / osb (oriented strand board)

## Slide 22: fiberboards - hdf / mdf / ldf

## Slide 23: Load dissipation

## Slide 24: horizontal bracing
OK
GOOD
GOOD
GOOD
Lack of strengh against twist
Lack of strengh against twist
Lack of stiffening in longitudinal direction
Lack of strengh against twist
Truss system
Frame system
disc system
core system

## Slide 25: connections

## Slide 26: carpentry connection
Blunt bump
Half lap
Mortise and tenon
Cross lap joint

## Slide 27: carpentry connection
Dovetail crossed lap
Face staggered joint
Notched housing
Obelique thrust joint with notched housing
Halved crossing joint

## Slide 28: engineering wood joints
shift
force
mechanical connection
(screws, sheets, steel parts)
Formfitting connection
glued connection

## Slide 29: Smooth nails
pin shaped connectors
But nails
Nail plates
brackets
screws
bolts
Fitting bolts
dowel
Self driling dowels

## Slide 30
Pin-shaped connetions

## Slide 31: Angle connector
System connectors
Beam shoe
Beam girder
Support base
Tension rod systems
Glued
connections
Perforated
steel strips

## Slide 32
Examples system connectors / sources
www.strongtie.de/products
www.rothoblaas.de/produkte/verbindungstechnik
www.pitzl-connectors.com/produkte
www.halfen.com/at/780/produktbereiche/bau/stabsysteme/detan-stabsystem/einfuehrung/
www.sfs.ch/de/Holzbefestiger
www.sihga.com/
www.schrauben.at/schraubenwelten/produkte/uebersicht
www.sherpa-connector.com

## Slide 33: elements

## Slide 34: research (elements)

## Slide 35: types of load bearing timber structures
Timber constructions systems (esp. housing)
cross laminated timber construction
timber frame construction
outside
inside
inside
outside
insulation
load bearing
insulation
load bearing
load bearing
Rod-shaped (across the grain)
load bearing
Rod-shaped
Flat-shaped (stiffening)
Flat-shaped
Block-construction
Cross laminated constr.
Half timberd construction (truss)
Timber frame construction

## Slide 36: Level of prefabrication
- Assembly of individual parts / Assembly of elements
Parts of the load-bearing structure and at least one layer are pre-assembled
The elements are insulated an planked on both sides, empty conduits (e.g. hose) for the building systems may be inserted
Elements including fixtures such as doors and windows, glazing are prefabricated
Elements including the facade structure, outer and inner cladding / facade are preassembled

## Slide 37: Types of construction - examples

## Slide 38: basic layering in timber construction
1 – Facade
2 – Shell construction / -element
3 – Inner panneling
1 – Floor construction
2 – Shell construction / -element
3 – Ceiling soffit

## Slide 39: examples - research

## Slide 40: example exterior wall - carpentry

## Slide 41: example exterior wall - industry

## Slide 42: example exterior wall – cross laminated

## Slide 43: example interior wall

## Slide 44: example compartment wall (between flats)

## Slide 45: example intermediate floor

## Slide 46: example intermediate floor (between flats) wohneinheiten)

## Slide 47: Example pitched roof

## Slide 48: digression - rules for a flat roof
(in the normal climate according to UNI EN 15026)
The roof has a slope ≥ 3% in “undeformed” configuration or ≥ 2% in “deformed” configuration under load
Dark-colored (radiation absorption ≥ 80%), with no shade
no covering layer (gravel, green roof, terraced lining)
a vapor barrier with sd variable to humidity (inner side)
no uncontrollable cavity on the cold side of the insulating layer and
perfect air tightness and
moisture content of the bearing elements including decking boards (u ≤ 15% ± 3%) or wooden finishes (u ≤ 12% ± 3%) must be checked before the roof is enclosed. These values must be carefully and appropriately documented.
7 golden rules for flat roofs
(without specific analysis)
Technical brochures (e.G. dataholz.eu
Hygro-
thermic-Simulation

## Slide 49: example flat roof

## Slide 50: example flat roof / terrace

## Slide 51: details

## Slide 52: examples

## Slide 53: Example corner

## Slide 54: Ceiling / partition wall
High sound transmission
reduced sound transmission (facing shell on the ceiling)
reduced sound transmission (separeted construction elements)

## Slide 55: separating ceiling / flat partition wall
In the case of wooden frames and wooden frame walls, as well as a suspended soffit of the ceiling
and decoupled cladding , no elastic bearings are required
With a suspended soffit on the ceiling and NO decoupled cladding on the walls, elastic bearings are recommended
on both sides - above and below
In the case of cross-laminated timber ceilings with a wooden soffit (without a suspended ceiling) and decoupled
cladding on the walls, elastic bearings above are recommended

## Slide 56: practise

## Slide 57: practise – ground plan

## Slide 58: Practise – cross section

## Slide 59: anforderungsprofil / aufgabenstellung
Ziele:
Niedrigstenergiestandard
Hochwertige Aufbauten in Bezug auf Schall (intern)
Abgesehen von Schallschutz mittlere Ausstattungsqualitäten
OIB-Richtlinie Niederösterreich
Definieren Sie gem. angegebene Anforderungsprofil nachfolgende Aufbauten:
Außenwand Außenwand
Flachdach
Steildach
Trennwand
Trenndecke
Auswertung durch Diskussion

## Slide 60: Source directory
Pech, Anton (Hrsg.) Holz im Hochbau, Springer Verlag
Wood Handbook, Wood as Engineering Material United Dep. Of Agriculture, Wisconsin, US
Manual for Engineered Wood Construction American Wood Concil
Richtlinie Sockelanschluss im Holzhausbau Holz Forschung Austria
Atlas Mehrgeschossiger Holzbau Edition Detail 2017
Auszug aus Vortragsreihe Modulbau rwt+ (Richard Woschitz)
www.proholz.at
www.dataholz.eu
www.frischeis.com
www.steico.com
www.clt.info
www.bruck33.at
www.strongtie.de/products
www.rothoblaas.de/produkte/verbindungstechnik
www.pitzl-connectors.com/produkte
www.halfen.com/at/780/produktbereiche/bau/stabsysteme/detan-stabsystem/einfuehrung/
www.sfs.ch/de/Holzbefestiger
www.sihga.com/
www.schrauben.at/schraubenwelten/produkte/uebersicht
www.sherpa-connector.com